## Slide 1: Memory Built-in-Self Test (MBIST): Analysis of Resistive-Bridging Defects in SRAM Core-Cells: a Comparative Study from 90nm down to 40nm Technology Nodes
ECE 7502 Class Discussion
Harsh N. Patel
02/19/2015

## Slide 2: Paper Map
[1] R. Alves Fonseca et. al. , "Analysis of Resistive-Bridging Defects in SRAM Core-Cells: a Comparative Study from 90nm down to 40nm Technology Nodes,“ ETS 2010.
[2] Van de Goor, A.J., et. al. "March LR: a test for realistic linked faults", 14th VLSI Test Symposium, 1996
[3] Hamdioui, S. et. al."Linked faults in random access memories: concept, fault models, test algorithms, and industrial results" ITC 2004.
[4] Zordan, L.B; et. al.;"On the reuse of read and write assist circuits to improve test efficiency in low-power SRAMs.” ITC 2013
[5] Zordan, L.B; et. al "Low-power SRAMs power mode control logic: Failure analysis and test solutions" International Test Conference (ITC), 2012.
[1] Targeting specific fault in memory core and its impact on complete array
[2] & [3] defines basic SRAM fault models
[4] use of existing peripherals for testing.
[5] Low Power SRAM power mode control logic testing.
Standard fault models for SRAM
Impact of subset of fault across tech and PVT
Different aspect of testing

## Slide 3
Requirements
Specification
Architecture
Logic / Circuits
Physical Design
Fabrication
Manufacturing Test
Packaging Test
PCB Test
System Test
PCB Architecture
PCB Circuits
PCB Physical Design
PCB Fabrication
Design and Test Development
Customer
Validate
Verify
Verify
Test
Test

## Slide 4: Outline
BIST: Basic functionality
Goal of the paper
Results
Stressing the bitcell [4]
Discussion questions

## Slide 5: Memory BIST
Basic functionality
Algorithms (Hard coded) + Decoding Logic +
Start/Stop Algo Control logic +
Bitmap for Failure Analysis (process maturity)
Input Generator
(Address , Data,
Rd/Wr Control)
Memory Under
Test
Output Comparator
+
Error Flag Generator

## Slide 6: Memory BIST
Goal of the paper:
A comparative study on the effects of resistive bridging defects in the SRAM.
Knobs:
Defect resistance size
Power supply
Memory size
Temperature
Technology

## Slide 7: Memory BIST
Fault Modeling Flow
Fault Detection
Defect locations extraction from the layout
Looking at adjacent lines of the same metal layer or between metal layers
Fault Simulation
Electrical simulations of defects
That leads to a faulty behavior of the SRAM
Fault Modeling
Generation of effective test algorithms
Modeling of the faulty behavior
Functional representation of faulty behavior.
Algorithm
Sequence of Wr/Rd pattern to detect the fault.

## Slide 8: Memory BIST
Targeted Fault: Resistive – Resistive Bridging Fault
Group | Fault | Impact
Group_1 | Df1 – Df3 | Single Cell
Group_2 | Df4 – Df5 | Double cells

## Slide 9: Memory BIST
Targeted Fault: Resistive – bridging Fault
Technology | Supply Voltage |  |  | Temp.
 | Low | Nom. | High | -40°C, -25°C, and -125°C
90nm | 1.0 | 1.1 | 1.2 | 
65nm | 0.9 | 1.0 | 1.1 | 
45nm | 0.8 | 0.9 | 1.0 | 

## Slide 10: Results
 | Fault Name
NSF | No Store Fault
RDF | Read Destructive Fault
WRF | Weak Read Fault
SAF | Struck-at Fault
IRF | Incorrect Read Fault
TF | Transition Fault
CFds | Disturb Coupling Fault
Higher values of resistances are susceptible to bridging defects (range increased).
Smaller technology are more susceptible to faults

## Slide 11: Results
Worst Case Condition(40nm)

## Slide 12: Results

## Slide 13: Case Study (1)
Impact of Df1: (inside the cell)
Target Fault: Read Destructive Fault (RDF) (Read operation disturbs the content)
Aim: To find the range of defect values in which RDF occurs.
Test case: Perform a read operation in transient simulations varying the defect value of Df1.
Failure Metric: Read Noise Margin

## Slide 14: Case Study (1)
Impact of Df1: (inside the cell)
Without Defect RSNM
With Df1= 150KΩ

## Slide 15: Case Study (2)
Impact of Df5: (among cells)
Target Faults: Weak Read Fault (WRF) (insufficient ΔBL for SA) and Incorrect Read Fault (IRF) (returned value is wrong while cell content is correct)
Test case: Perform a read operation in transient simulations varying the defect value of Df5 while looking at the cell content.
Failure Metric: Read Noise Margin

## Slide 16: Case Study (2)
Impact of Df5: (among cells)
Normal Read Operation.
possible Weak Read Fault
Incorrect read Faults

## Slide 17: Stressing the Cell [4]
RB = Resistive Bridging Fault
RO = Resistive Open Fault
Setup:
Industry standard 6T cell layout of 40nm node
Supply Voltage: 1.1V & 1.0
Assist Techniques:
  Wordline reduction (WLR) (for read)
  Negative Bitline(NBL) (for write)
  Goal:
  Find Worst case Configuration for Assist circuit (WCA)

## Slide 18
Stressing the Cell [4]
Notes: 1. Faulty cell has RNM1 that is lower than RNM1
of a defect-free cell.
2. Presence of Df3_RO drastically degrades RNM1 of core-cells.

## Slide 19
Stressing the Cell [4]
Notes:  Df1_RO degrades WM1 of
core-cells.
Faulty cell has a higher WM1, when WLR is either in normal mode or
disabled, compared to the WM1 of a defect-free core-cell, when WLR is in strong mode.
 Drastically WM is impacted by the use of WLR assist circuit.

## Slide 20
Stressing the Cell [4]

## Slide 21
The algorithm with assist configuration that exercise the worst case scenario for RO faults and RB faults.
Stressing the Cell [4]

## Slide 22: Conclusion / Take away
Finding worst case PVT for particular technology helps reducing testing time by limiting the test run to the worst case corner rather validating across the corners.
Stressing the cell while testing finds failures those are difficult to observe otherwise.

## Slide 23: Discussion questions
How to evaluate the completeness of the fault simulation?
With possible non-uniform worst-case scenarios across different faults, how can we reduce the test-time?
Is there any design parameter (except Height) that impact the functionality?
Is there any other way to stress the cell for the testing without changing external inputs?
What type of tests an SRAM designer should performed preemptively to minimize the failures?

## Slide 24: Papers
[1] Fonseca, R.A. ; Dilillo, L. ; Bosio, A. ; Girard, P. ; Pravossoudovitch, S. ; Virazel, A. ; Badereddine, N., "Analysis of resistive-bridging defects in SRAM core-cells: A comparative study from 90nm down to 40nm technology nodes", 15th European Test Symposium (ETS), 2010 pdf
[2] Van de Goor, A.J.; Gaydadjiev, G.N.; Mikitjuk, V.G.; Yarmolik, V.N., "March LR: a test for realistic linked faults", 14th VLSI Test Symposium, 1996 pdf
[3] Hamdioui, S.; Al-Ars, Z.; van de Goor, A.J.; Rodgers, M., "Linked faults in random access memories: concept, fault models, test algorithms, and industrial results," IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems, 2004 pdf
[4] Zordan, L.B.; Bosio, A.; Dilillo, L.; Girard, P.; Todri, A.; Virazel, A.; Badereddine, N., "On the reuse of read and write assist circuits to improve test efficiency in low-power SRAMs" ITC 2013 pdf
[5] Zordan, L.B.; Bosio, A.; Dililo, L.; Girard, P.; Todri, A.; Virazel, A.; Badereddine, N., "Low-power SRAMs power mode control logic: Failure analysis and test solutions" International Test Conference (ITC), 2012 pdf